## Slide 1: Using Health Hazard Bands to Assess Risk and Design, Implement and Evaluate Control Solutions
Donna S. Heidel, MS, CIH
CDC/NIOSH
Prevention through Design Coordinator
2011 Toxicology and Risk Assessment Conference
New Methods and New Hazards in Toxicology and Risk Assessment

## Slide 2: Topics for discussion
Value of health hazard banding and control banding to effective, comprehensive risk management
Value to Prevention through Design
NIOSH/AIHA/stakeholder hazard banding activities

## Slide 3
Best way to manage occupational exposures to chemical agents is to eliminate the hazard or “design out” the risk
Elimination
Substitution
Engineering controls

## Slide 4: Scope of challenge to manage worker exposure to chemicals
~35,000,000 organic and inorganic substances
~21,000,000 commercially available chemicals
107,067 REACH* registrations (1-3-11) for >1000 tons production volume or those of high concern
  More chemicals will be registered for the >1 ton amounts through various deadlines ending in 2018
*REACH – Registration, Evaluation, Authorization, and Restriction of Chemicals
BUT… there are ~ 500 PELs, ~ 650 RELs,~ 125 WEELs, ~ 650 TLVs
Notes: The sheer volume of chemicals in production and use is motivation enough to seek additional chemical risk management strategies:
More than 35 million organic and inorganic substances
21 million commercially available chemicals
246,000 inventoried and regulated substances, and
170,000 chemicals that may require registration under REACH regulations
(Next slide)

## Slide 5
How can we “design out” hazards if we haven’t identified or categorized them?
How can we “design in” controls if we haven’t assessed the potential risk from task-based occupational exposures?

## Slide 6: Background: health hazard bands
Based on the NIH/CDC Biosafety Level model
Concept developed by the pharmaceutical industry in 1980s
  Increased specificity of investigational new drugs
    Increased potency and increased potential for occupational toxicity
  High throughput screening increased the number of investigational new drugs in research labs and pilot plants
Assign chemicals into “categories” or “bands” based on their inherent properties
Facilitates the implementation of “control bands”
Not a substitute for OELs or exposure monitoring surveys

## Slide 7: Risk Management Paradigms*
Traditional Risk Management
Hazard Exposure Control
Control Banding Risk Management
Hazard Control Exposure (control verification)
*Keith Tait, Corporate Health & Safety, Pfizer - National Control Banding Workshop, Washington, DC, March 2005
Notes: What was most significant and distinguishing about these models was the paradigm shift from the traditional risk assessment/management model. Instead of following an approach wherein risk was determined based on hazard identification, exposure assessment, and subsequent determination of control options, the new approach (here called the pharmaceutical model) assessed and managed risk by following the hazard ID stage with the implementation of control, then evaluated the effectiveness of the control with exposure assessment as necessary. (next slide)

## Slide 8: Hazard banding value to NIOSH
Efficiency of REL and WEEL development is outpaced by the speed of new chemical introduction into commerce
  Limited human and financial resources; may be limited data
  Intensive process to assure accurate interpretation of data
Can be used with minimal data
Supports the definition of OEL-ranges for families of materials
  By analogy (structure activity relationships and functionality)
Provides a screening tool for the development of OELs
Highlights areas where data are missing
Notes: Efficiency of REL development is outpaced by the speed of new chemical introduction into commerce
  Limited human and financial resources
  Insufficient data
  Intensive process to assure accurate interpretation of data
Can be used with minimal data
Supports the definition of REL-ranges for families of materials where the data or resources are too limited to allow for a comprehensive and conclusive assessment of risk
  By analogy (structure activity relationships and functionality); e.g., diacetyl, 2,3-pentanedione and other flavorings
Provides a screening tool for the development of RELs
Highlights areas where data are missing

## Slide 9: Hazard banding value to industrial hygienists
Provides guidance for materials without authoritative OELs
Identifies hazards that should be evaluated for substitution
Aligned with globally harmonized system for hazard communication
Logical approach for initiating Control Banding
  i.e., linking to task-based, control-focused solutions
Facilitates the application of PtD to eliminate hazards and minimize risks to chemical agents
Notes: The OSHA Hazard Communication standard incorporating the Global Harmonization System estimated that there are 880,000 hazardous chemicals in current use.
ECHA reported that by the Jan 3, 2010 deadline REACH received 3,114,835 notifications of 107,067 substances for the Classification and Labeling Inventory which covers only the greater than 1000 tons production volume or those of high concern, e.g. carcinogens, mutagens and reproductive toxins. More chemicals will be registered for the >1 ton amounts through various deadlines ending in 2018.
OSHA currently regulates ~ 500 chemicals, based mostly on science from the 1950s and 1960s. (NIOSH has ~650 RELs, compared to Worldwide OELs ~1300).
From a sample of 2360 REACH registrations collected early in 2010, NIOSH/OSHA covered only 278 11.7%) of these registrations with RELs/PELs.

## Slide 10: Project overview
Health-, eco hazard-, and fire/explosion-hazard bands
For health hazard bands, the following criteria are included:
  WEEL banding criteria
  HSE/ILO categories and R-phrases
  GHS hazard statements and criteria
  Green screen
  ANSI combined standard
  Industry models

## Slide 11
Supplement RELs with Health Hazard Bands
EID Leadership: NIOSH Guidance, Process and Tools
Extramural Experts
Industry Collaborators
NIOSH/AIHA Alliance
ANSI Standard: Health Hazard Banding  Control Banding
Integration into Z-10 (Management Systems)
Educate NIOSH on industry process; provide examples; tool validation process
AIHA, EPA, Labor, OSHA, Industry and Individual Contributors
Improved Chemical Risk Management

## Slide 12: Expected project outputs
Guidance document including
  criteria to group chemicals into bands
  links to control bands
  impact on worker health and organizational benefits
  integration into H&S management systems
Overall process, including the decision logic
Tools to facilitate evaluating hazard data and assign chemicals to hazard bands
Education materials for H&S professionals, managers, and workers
Long term: database of chemical hazards
Notes: Guidance document providing a history of hazard banding, the criteria to group chemicals into bands, the links to control bands, the impact on worker health, the organizational benefits, and the integration into H&S management systems
Overall process an organization may use to implement hazard banding, including the decision logic
Tools to facilitate evaluating hazard data and assign chemicals without authoritative OELs into hazard bands
Education materials for H&S professionals, managers, and workers

## Slide 13: Work in progress
Finalizing criteria and bands
Developing process and decision logic
  Qualitative/semi-quantitative algorithms
Validation plan for process and decision logic
Overall guidance document
Education modules
  Workers and managers
  EHS professional
Database of hazard information for chemicals

## Slide 14
DRAFT Hazard Banding Summary including AIHA WEEL Banding Matrix, HSE/ILO categories and R-phrases, GHS Hazard Statements and Criteria, ANSI Combined Standard, Industry bands, Green Screen, and Clean Production Action |  |  |  |  | 
4/20/2011 version 1.4 |  |  |  |  | 
Band | A | B | C | D | E
Signal Word | Warning | Warning | Danger | Danger | Danger
Hazard Statement | May be Harmful | Harmful | Toxic | Very Toxic/Fatal | Fatal
OEL Range | > 1,000 µg/m3 | > 100 and < 1,000 µg/m3 | > 10 and < 100 µg/m3 | > 1 and < 10 µg/m3 | < 1 µg/m3
Risk Phrases banded according to the HSE & ILO Toolkit (inconsistencies with other banding methods and the Hazard Banding team's recommendations and indicated in red font) | 36; 38; 36/38; 65; 66; All substances that do not have R phrases in groups B - E | 20; 20/21; 20/21/22; 20/22; 21; 21/22; 22; 40/20/21/22; 33; 67 | 23; 23/24; 23/24/25; 23/25; 24; 24/25; 25; 34; 35; 36/37; 36/37/38; 37; 37/38; 41; 43; 48/20; 48/20/21; 48/20/21/22 48/20/22; 48/21; 48/21/22; 48/22; 39/23/24/25 | 26; 26/27; 26/27/28; 26/28; 27; 27/28; 28; Carc Cat 3 R40; 48/23; 48/23/24; 48/23/24/25; 48/23/25; 48/24; 48/24/25; 48/25; 60; 61; 62; 63; 64; 39/26/27/28 | Muta Cat 3 R40; 42; 42/43; 45; 46; 49; 68
Health Risk Phrases not mentioned in HSE and ILO Toolkit |  |  | 39, 39/23, 39/23/24. 39/23/25, 39/24, 39/24/25, 39/25, 68/20, 68/20/21, 68/20/21/22. 68/20/22, 68/21, 68/21/22, 68/22 | 39/26, 39/26/27/28, 39/26/28, 39/27, 39/27/28, 39/28, 48 | 
GHS phrases (HSE & ILO Toolkit) | Acute toxicity (lethality), any route, class 5; Skin irritancy class 2 or 3; Eye irritancy class 2; All dusts and vapors not allocated to another band | Acute toxicity (lethality), any route, class 4; Acute toxicity (systemic), any route, class 2 | Acute toxicity (lethality), any route, class 3; Acute toxicity (systemic), any route, class 1; Corrosivity, subclass 1A, 1B or 1C; Eye irritancy class 1; Respiratory system irritancy (GHS criteria to be agreed); Skin sensitization; Repeated exposure toxicity, any route, class 2 | Acute toxicity (lethality), any route, class 1 or 2; Carcinogenicity class 2; Repeated exposure toxicity, any route, class 1; Reproductive toxicity class 1 or 2 | Mutagenicity class 1 or 2; Carcinogenicity class 1; Respiratory sensitization

## Slide 15
Potential Impacts

## Slide 16: Supports inclusion of H&S in the engineering project delivery process
Stage | Activities
Conceptual Design | Establish occupational safety and health goals, identify occupational hazards
Preliminary Design | Eliminate hazards, if possible. Substitute less hazardous agents / processes, and establish risk minimization targets for remaining hazards. Assess risk and develop risk control alternatives.
Detailed Design | Select controls. Conduct Process Hazard Reviews.
Procurement | Develop specifications and include in procurements. Develop test protocols for factory acceptance testing and commissioning
Construction | Construction site safety and contractor safety.
Commissioning | Conduct tests including factory acceptance. Pre-start up safety reviews. Development of SOPs. Risk / exposure assessment. Management of residual risks.
Start Up and Occupancy | Education. Management of change. Modification of SOPs

## Slide 17: Ability to influence H&S design
(Source: Szymberski, R., “Construction Project Safety Planning.” TAPPI Journal, Vol. 80, No. 11, pp. 69-74.)
Conceptual Design
Detailed Engineering
Procurement
Construction
Start-up
High
Low
Start date
End date
Ability to Influence H&S
Project Schedule
Cost
Notes: In 1997, Szymberski offered that our ability to influence safety drops off dramatically as we get into detailed engineering. My own experience in industry (designing for IH risk minimization in the pharmaceutical industry) was that our ability to influence dropped off even more dramatically if we were not present at conceptual design. This is due to budgeting that typically occurs during conceptual design. Costs also dramatically increase if we make design modifications during detailed engineering.

## Slide 18
Exposure Risk
Physical Form
Task Duration
Quantity
milligrams
kilograms
15 minutes
8 hours
slurry/suspension
highly disperse
agglomerated
Factors Influencing Control Design/Selection
Engineered Local Exhaust Ventilation
Closed Systems
Occupational Health Hazard
mild / reversible
severe / irreversible

## Slide 19
Exposure Risk
Physical Form
Task Duration
Quantity
milligrams
kilograms
15 minutes
8 hours
slurry/suspension
highly disperse
agglomerated
Factors Influencing Control Selection
Engineered Local Exhaust Ventilation
Closed Systems
Occupational Health Hazard
mild / reversible
severe / irreversible

## Slide 20: Supports selection of risk-based controls
Known or anticipated health hazards of material
Factors influencing exposure risk
  Physical form, task frequency and duration, etc.
Scale of operations
  Laboratory / pilot scale
  Production of the chemical or mixture
  Product formulation with the chemical or mixture
Known performance of controls
  E.g., finely-divided powders or gases
  Test expected performance using surrogates
Incomplete health hazard datasets prompt conservative control approaches

## Slide 21: And supports design of other appropriate controls
Process and process equipment
Facility design, including room finishes
Room configuration
Mechanical systems, including ventilation, dust collection, area pressurization
Equipment cleaning
Equipment maintenance
Gowning/gown-down
Work practice/work organization controls
Management of change
Industrial hygiene / occupational health support

## Slide 22: Incomplete health hazard data
Consider these prudent practices
Handle materials as slurries or suspensions
  When possible, wet materials after weighing, before removing from hood or containment system
Use closed systems for loading and unloading materials from process equipment
Place lab scale equipment into ventilated enclosures
Control particle migration via ventilation system or contaminants on people and equipment
Cover street clothing or change into work uniforms
Use redundant PPE

## Slide 23
The findings and conclusions in this presentation have not been formally disseminated by the National Institute for Occupational Safety and Health and should not be construed to represent any agency determination or policy