## Slide 1
Nonverbal Communication for Mine Emergencies
Signal Training Program

## Slide 2: In the Event of an Emergency
If you have your SCSR on, you must not remove it to talk.
Removing it will expose you to dangerous gases that may kill you.
In addition to using cap lamp signals and writing notes using pen & paper, chalk, or writing in rock dust, new nonverbal hand signals have been created to help miners communicate while wearing SCSRs.

## Slide 3: Hand Signals

## Slide 4: Yes/Good Idea
Thumbs up

## Slide 5: No/Bad Idea
Thumbs down

## Slide 6: You/It/Them/There
Point at person(s) or thing(s)

## Slide 7: I/Me
Point at yourself

## Slide 8: We/Us
Point finger up, move in circular motion

## Slide 9: Stop/Stay Here
Arm straight out, slightly angled toward floor, palm facing forward

## Slide 10: Go This Way
Arm at side, extend outward from waist indicating direction, palm facing out

## Slide 11: Don’t Know/Don’t Understand
Hold both hands out at shoulder height with palms up, shrug

## Slide 12: SCSR
Put hand in front of face, palm facing you

## Slide 13: Refuge Chamber/Barricade
Touch fingertips to make triangle in front of chest

## Slide 14: Refuge Chamber/Barricade (One Handed)
Create half of a triangle in front of chest

## Slide 15: Gas Detector/Gas Readings
Simulate holding gas detector up to the roof

## Slide 16: A Problem
Palm facing forward, move hand to and away from top of head

## Slide 17: Follow Me/Come This Way
Bend lower arm to bring hand up toward self; beckoning motion

## Slide 18: Slow Down
Slowly lower hand, palm facing down

## Slide 19: Evacuate
Move bent arms back and forth next to body (running motion)

## Slide 20: Evacuate (One Handed)
Move bent arm back and forth next to body (running motion)

## Slide 21: Lifeline/Tether
Arm at side with elbow bent 90 degrees to front,
move hand as if grasping line

## Slide 22: Phrases
Multiple signals can be strung together to produce a phrase.

## Slide 23: Sample Phrase 1
We should evacuate. Follow me to the lifeline.

## Slide 24: Sample Phrase 2
We should go this way to the refuge chamber.

## Slide 25: Phrase 2 (with glowstick, in smoke)
We should go this way to the refuge chamber.

## Slide 26: Helpful Hints
Pausing between hand signals is often necessary to make sure the message you are trying to communicate is clear.
When one miner is using hand signals, other miners should pay attention to what he or she is trying to communicate.

## Slide 27: Helpful Hints
There are no hand signals for punctuation.
It might be unclear if you are asking a question or making a statement.
Therefore, miners should respond to every hand signal message received.
  Example: Joe performs the hand signal for “refuge chamber.” Other miners should respond with the hand signal for “yes/good idea” or “no/bad idea” with the assumption that Joe was asking whether or not you should go to the refuge chamber.

## Slide 28: Helpful Hints
If hand signals cannot be seen because of smoke or distance, miners have three options:
  If there is smoke and another miner is in close proximity, put the other miner’s hand over yours to communicate the signal effectively.
  If you have one, hold a glowstick when using the signals.
  If you are at a distance from other miners, use your cap lamp signals.