## Slide 1: Radio 101
Everyday and Emergency
Radio Use

## Slide 2: Background
Past difficulties with radio use
  What problems have you had with radios?
Following some “Rules of the Radio” ensures everyone can use the radio effectively
  Especially important for emergencies

## Slide 3: Types of Radio Traffic
Routine traffic
Emergency traffic
Mayday traffic

## Slide 4: How To Use The Radio Everyday
Push and hold the button before starting to talk.
Wait a few seconds before you start talking.
Hold radio 3–4 inches from your mouth.
Do not yell into the radio.
Speak slowly and clearly.

## Slide 5: How To Use The Radio Everyday
Remember: only one person can talk at a time.
Be brief and efficient.
  Reduce the use of air time as much as possible.
  Use a standard protocol for speaking.

## Slide 6: What to Say
Communicate where you are located and your message.
  Use location identifiers (e.g., Crosscut #).
Repeat back what you heard to ensure you got the message right.

## Slide 7: How to Say It
Sender: “Hey Fred, it’s me George.”
Receiver: “Go ahead George.”
Sender: “State your message.”
Receiver: Repeat information back.
Sender: Correct or confirm.
Receiver: Says how they will respond.

## Slide 8: Example
Mike (section mechanic): “Joe, this is Mike.”
Joe (maintenance foreman): “Go ahead Mike.”
Mike: “When you come on the section, bring 5 shuttle car cable splice kits.”
Joe: “You want 5 shuttle car cable splice kits?”
Mike: “Yes, bring 5.”
Joe: “Will do.”

## Slide 9: Tips for Everyday Use
Efficiency is more important than politeness.
Avoid jargon and codes.
Use established protocols.
Be brief, listen, speak clearly, acknowledge receipt of information.
Only transmit pertinent information.
Keep radio with you at all times.
Be aware that people who are not your intended audience may overhear you.

## Slide 10: Tips for Everyday Use, continued
Limit to essential communication.
  Do not have personal chats.
  Do not talk too much.
Do not swear or shout.
Many wireless systems are line-of-sight.
  If possible, move to a location which allows you to transmit in a line-of-sight to the next radio.
Antennas can be easily damaged; protect them as much as possible.

## Slide 11: Emergency Radio Use
Past difficulties with radio use in emergencies
  What problems have you had with radios?
Following some “Rules of the Radio” ensures everyone can use the radio effectively.
  Especially important for emergencies

## Slide 12: Tips for Emergency Use
Ask for radio waves by saying “emergency traffic” or “mayday, mayday, mayday.”
Identify yourself.
Identify your location.
Briefly describe the emergency.

## Slide 13: Tips for Emergency Use, continued
Provide details:
  about the miners who are involved (WHO)
  about the location of the event (WHERE)
  about the event—injuries, damage, fire (WHAT)
  about the response that is going on.
If you are bringing someone out, ask dispatch or responsible person to clear vehicle traffic.

## Slide 14: Example of Standard Protocol in an Emergency
Crew A: “Emergency traffic, this is Crew A.”
Dispatch: “Go ahead Crew A.”
Crew A: “We’ve got a fire on the belt inby of Crosscut 87.”
Dispatch: “Belt fire inby crosscut 87.”
Crew A: “Confirm that.”
Dispatch: “Evacuate the mine. We are calling the responsible person.”

## Slide 15: Points About Messages
Most messages consist of:
  Orders and instructions for controlling the situation
  Reports about the conditions and progress
  Requests for additional resources

## Slide 16: Points About Messages, continued
Every message must be clear, concise, and timely.
Provide regular status reports or updates
  First update about 10 minutes after initial report
  Subsequent updates every 10–15 minutes OR whenever a significant escalation occurs.

## Slide 17: Wireless Communications Systems
What type of communications systems do you have at your mine?

## Slide 18: Leaky Feeder
All communication runs through the “head end,” which is on the surface.
If there is a break in the line, anyone inby the break will not be able to use the system.
  If there is an alternate line, miners can use it to communicate despite the break in the main line.
If two mics are keyed together, there is a warning tone.

## Slide 19: Medium Frequency
Uses any available metal as a transmitter
  Pager phone wire
  Water pipes
  Power lines
Has a delay of 1–2 seconds or more.
  Must wait extra time for the message to come back.
  If both mics are keyed at same time, neither message goes through.

## Slide 20: Through-The-Earth (TTE)
Antenna is a long, looped wire.
The bigger you make the circle enclosed by the antenna, the better the reception you will get.